## Slide 1: 5G Waveform Modulation & Demodulation
Prepared By:
Tawsif Ahmad Thakur Bhattarai Luvpreet Kaur

## Slide 2
5G Overview
High Data Rate (can achieve 1.4 Gbps median speed for 28GHz mmWave)
Low communication Latency (about 1ms.)
High Bandwidth efficiency
High user density
5G waveforms are basically OFDM signals.
Waveforms are strengthened by using Baseband filtering
Transmission is done incorporating MIMO technologies

## Slide 3
5G Block Diagram
5G uses OFDM along with some specific features
Binary Data
Symbol Mapping
Block
IFFT
Add Cyclic Prefix
Random Channel
Figure : Transmitter Side

## Slide 4
5G Block Diagram
Received Signal from channel
Remove
Cyclic
Prefix
Block
FFT
Detection
Detected Symbols
Figure : Receiver Side

## Slide 5
Some Parameters
FFT/IFFT Block size = 32
Number of FFT/IFFT Blocks = 50
Cyclic Prefix Length = 20
White Noise SNR = 18 dB
Baseband Filter Length = 513
Baseband Filter Type: Windowed Sinc function Prototype filter

## Slide 6
Symbol Mapping
We used QPSK modulation (Gray encoding)
00
01
11
10
Bit Pair | Symbol
00 | 1
01 | j
11 | -1
10 | -j

## Slide 7
PSD of Modulated Waveform

## Slide 8
Symbol Detection
For symbol detection, we used the G matrix
G = fft([channel(2:end) . . . 0 …. 0 channel(1)]);
Then, we performed element-wise division between each CP removed FFT block output and the G matrix

## Slide 9
5G OFDM with 16-QAM
For 16-QAM, symbol mapping is done as follows:
 | I |  | Q
00 | -3 | 00 | -3
01 | -1 | 01 | -1
11 | +1 | 11 | +1
10 | +3 | 10 | +3
 | I |  | Q
00 | -3 | 00 | -3
01 | -1 | 01 | -1
11 | +1 | 11 | +1
10 | +3 | 10 | +3

## Slide 10
PSD of transmitted signal in case of 16-QAM
PSD has an average value of around -15 dBW/Hz whereas in the QPSK case, it was around -25 dBW/Hz. So, we can say that, PSD significantly improves for 16-QAM. It can be improved by implementing higher order QAM such as 64-QAM or 256-QAM.

## Slide 11
PSD of Detected Signals
QPSK case
16-QAM case
We observe significant improvements in the detected signal PSD in case of 16-QAM over QPSK which was the expected result.

## Slide 12
16-QAM Detection
We implemented the same G-matrix approach for detection of 16-QAM Symbols as we did for QPSK

## Slide 13
Baseband Filtering
Transmitted signal is filtered before passing through the channel and in the receiver side a matched filter is used before CP deletion and FFT.
OFDM Transmitter
Filter
CHANNEL
Matched
Filter
OFDM Receiver
Figure: Block Diagram of OFDM transmission with Baseband Filtering

## Slide 14
QPSK + Filtered OFDM
F-OFDM
OFDM

## Slide 15
QPSK + Filtered OFDM (contd…)

## Slide 16
16-QAM + FOFDM
F-OFDM
OFDM

## Slide 17
16-QAM + FOFDM (contd…)

## Slide 18
MIMO Communication
We considered 4×4 MIMO Communication System
F-OFDM Transmitter
TX #1
TX #2
TX #3
TX #4
RX #1
RX #2
RX #3
RX #4
F-OFDM Receiver
Figure: MIMO F-OFDM System

## Slide 19
Received Signal PSD Comparison
(With & without MIMO)
Without MIMO
With MIMO

## Slide 20
MIMO Symbol Detection
For SNR = 18 dB
For SNR = 22 dB

## Slide 21
Effect of Noise
Due to noise, signal detection deteriorates. The following figures explain this claim.
16-QAM F-OFDM MIMO with noise (22 dB)
16-QAM F-OFDM MIMO without noise

## Slide 22
Conclusion
We observed 5G OFDM communication system with QPSK used for symbol mapping and observed the PSD of the TX and RX signals
Then, instead of QPSK, we implemented 16-QAM modulation and observed the concerning outputs and compared the results
Then we implemented Baseband Filtering (FOFDM) for both the QPSK and 16-QAM modulations and compared the results
We implemented 4×4 MIMO on the existing F-OFDM system and observed that for MIMO, higher SNR is needed.
Currently, we are working on the MIMO system to get better result in terms of the detected symbols with minimum SNR.

## Slide 23
THANK YOU